Secure Sequence Recognizer

Author:Iacopo Pacini

# Introduction
The device implemented is a synchronous sequence recognizer, the sequence numbers are five 8-bit integers. At the beginning of the process the signal must be set to '1' for one clock cycle and the following must be send to the SSR at the rate of 1 clock cycle.
The “first” pin must be kept high for no more than 1 clock cycle otherwise the SSR stops working until a future reset.
The sampling duration is always five clock cycles long and at the end the pin “unlock” is kept high for one clock cycle if the sequence has been inserted correctly.
Instead,if there is at least a wrong number in the sequence the pin “warning” goes to '1' for a clock cycle.
If it is being inserted a wrong sequence more than three times consecutively the SSR stops working and “warning” goes to '1' permanently or at least until the input pin “reset” goes to '0'

Picture 1: An I\O view of the device
Secure
Sequence
Recognizer

8
num_in

first
reset
clock
unlock
warning

# Architecture
The SSR is a finite state machine whose state is described in the STAR register,the latter is a 3-bit register and the possible state are:
1. SINIT:the SSR in this state waits for the first sequence number and enter this state whenever the pin “reset” goes to '1'
2. S0,S1,S2,S3,S4:In each of those states the SSR samples the input sequences and checks for their correctness
3. S5:In this state the “unlock” pin is set to '1' if there were no input errors otherwise the 'warning' pin goes to '1' for a clock cycle.
4. SBLOCK: The SSR enters this state whenever the 'first' pin is kept high too long or in the wrong moment and if the sequence is inserted incorrectly for at least three consecutive times. The device leaves this state only if the 'reset' becomes high.
Some other tools are needed in order to make a correct sampling:
- OK.: 1-bit register that contains 1 if until now the sequences are correct, otherwise 0.
- lut_seq: Lookup table that contains the correct sequence.
- SEQNUMBER: 3-bit counter that drives the input of lut_seq.
- COUNT_WRONG:2-bit counter that counts the number of consecutive wrong inputs.

## State Diagram

Picture 2: SSR State diagram
Next clock
Next clock
S5

Unlock=?
Warning=?
S0

Unlock=0
warning=0
SINIT

Unlock=0
Warning=?
S4

Unlock=0
warning=0
SBLOCK

Unlock=0
warning=1
S1

Unlock=0
warning=0
S3

Unlock=0
warning=0
S2

Unlock=0
warning=0

Reset=0 or first=0

first=1

reset=1

Next clock

Next clock
Next clock
Next clock

first=1
first=1
first=1
first=1
count_wr_out="11" or

reset=0

# Code
## Secure Sequence Recognizer
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use ieee.numeric_std.all;

entity SecureSequenceRec is
port (
clock:	in std_logic; --- clock signal
reset:	in std_logic; -- reset signal active low
first:	in std_logic; -- start sampling signal
num_in:	in std_logic_vector(7 downto 0); --input sequence number

unlock:	out std_logic; -- signal of success
warning: out std_logic -- error signal

);
end SecureSequenceRec;

architecture SSR_beh of SecureSequenceRec is
SUBTYPE STATE_TYPE_COUNT is STD_LOGIC_VECTOR (1 DOWNTO 0) ;
CONSTANT SMEM: STATE_TYPE_COUNT :="00"; -- when in this state the counter just keeps the exit constant
CONSTANT SINC: STATE_TYPE_COUNT :="01"; -- when in this state the counter increments the exit
CONSTANT SRES: STATE_TYPE_COUNT :="11"; -- when in this state the counter keeps the exit equals to zero

SUBTYPE STATE_TYPE is STD_LOGIC_VECTOR (2 DOWNTO 0) ;
-- constants to drive the state
CONSTANT SINIT: STATE_TYPE:="000";
CONSTANT S0: STATE_TYPE:="001";
CONSTANT S1: STATE_TYPE:="010";
CONSTANT S2: STATE_TYPE:="011";
CONSTANT S3: STATE_TYPE:="100";
CONSTANT S4: STATE_TYPE:="101";
CONSTANT S5: STATE_TYPE:="110";
CONSTANT SBLOCK: STATE_TYPE:="111";

signal signal_star_in : STATE_TYPE;
signal signal_star_out : STATE_TYPE;

signal lut_in : std_logic_vector(2 downto 0);
signal lut_out : std_logic_vector(7 downto 0);

signal signal_ok_in : std_logic_vector(0 downto 0);
signal signal_ok_out : std_logic_vector(0 downto 0);-- 0 when a wrong number is inserted

signal count_wr_in : STATE_TYPE_COUNT; -- count the wrong sequences
signal count_wr_out : std_logic_vector(1 downto 0);

signal counter_state_in : STATE_TYPE_COUNT;

component DFF is
generic(N_bit : integer);
port (
clk: in std_logic;
reset: in std_logic;
D: in std_logic_vector(N_bit-1 downto 0);
Q: out std_logic_vector(N_bit-1 downto 0)
);
end component;

component LUT is

port(
address : in STD_LOGIC_VECTOR(2 downto 0);
data : out STD_LOGIC_VECTOR(7 downto 0)
    );
end component;

component Counter_mod is
generic(N_bitc : integer);
port(
count_clk	: in	STD_LOGIC;
count_reset	: in	STD_LOGIC;
enabler_in	: in	STD_LOGIC_VECTOR(1 DOWNTO 0) ;
D_out	: out	STD_LOGIC_VECTOR(N_bitc-1 downto 0)
    );

end component;

begin

OK: DFF --1 if the seq number is correct,0 otherwise
generic map(N_bit => 1)
port map(clock,reset,signal_ok_in,signal_ok_out);

STAR: DFF --status register
generic map(N_bit => 3)
port map(clock,reset,signal_star_in,signal_star_out);

SEQNUMBER: counter_mod --Drives the lut
generic map(N_bitc => 3)
port map(clock,reset,counter_state_in,lut_in);

COUNT_WRONG: counter_mod --Keeps track of the wrong sequences
generic map(N_bitc =>2)
port map(clock,reset,count_wr_in,count_wr_out);

lut_seq : LUT --contains the sequence numbers
port map(lut_in,lut_out);

LOGIC:process(signal_star_out,reset,first)
begin
if(reset='0') then
signal_star_in<=SINIT;
unlock<='0';
warning<='0';
signal_ok_in<="0";
counter_state_in<=SRES;
count_wr_in<=SRES;
else
case(signal_star_out) is
when SINIT=> -- the SSR in this state waits for the first sequence number
unlock<='0';

if(first='1' ) then
signal_star_in<=S0;
counter_state_in<=SINC;	--start counting
else
signal_star_in<=SINIT;
counter_state_in<=SMEM;
end if;
warning<='0';
count_wr_in<=SMEM;
signal_ok_in<="0";
  when S0 =>
count_wr_in<=SMEM;
unlock<='0';
warning<='0';
signal_star_in<=S1;

if(num_in = lut_out ) then --Checking Sequence number 0
signal_ok_in<="1";
else
signal_ok_in<=signal_ok_out;
end if;

counter_state_in<= SINC;
when S1 =>
unlock<='0';
warning<='0';
count_wr_in<=SMEM;
if(first='1')then --From now on it is an error if first goes to '1' and the device is being blocked
signal_ok_in<="0";
signal_star_in<=SBLOCK;
else
if(num_in = lut_out)then --Checking Sequence number 1
signal_ok_in<=signal_ok_out;
else
signal_ok_in<="0";
end if;
signal_star_in<=S2;
end if;
counter_state_in<= SINC;
when S2=>
unlock<='0';
warning<='0';
count_wr_in<=SMEM;
if(first='1')then
signal_ok_in<="0";
signal_star_in<=SBLOCK;
else
if(num_in = lut_out)then --Checking Sequence number 2
signal_ok_in<=signal_ok_out;
else
signal_ok_in<="0";
end if;
signal_star_in<=S3;
end if;
counter_state_in<= SINC;
when S3=>
unlock<='0';
warning<='0';
count_wr_in<=SMEM;
if(first='1')then
signal_ok_in<="0";
signal_star_in<=SBLOCK;
else
if(num_in = lut_out)then --Checking Sequence number 3
signal_ok_in<=signal_ok_out;
else
signal_ok_in<="0";
end if;

signal_star_in<=S4;
end if;
counter_state_in<= SMEM;
when S4=>
unlock<='0';
warning<='0';
count_wr_in<=SMEM;
if(first='1')then
signal_ok_in<="0";
signal_star_in<=SBLOCK;
else
if(num_in = lut_out)then --Checking Sequence number 4
signal_ok_in<=signal_ok_out;
else
signal_ok_in<="0";
end if;
signal_star_in<=S5;
end if;
counter_state_in<= SRES;
when S5 =>
unlock<= signal_ok_out(0);
warning <= not signal_ok_out(0);
if(signal_ok_out(0)='1') then
count_wr_in<=SRES;
else
count_wr_in<=SINC;
end if;
counter_state_in<= SRES;
if(first='1' or (signal_ok_out(0)='0' and count_wr_out="10" )) then
signal_star_in<=SBLOCK;
else
signal_star_in<=SINIT;
end if;
signal_ok_in<="0";
when SBLOCK=>
unlock<='0';
warning<='1';
signal_star_in<=SBLOCK; --Blocking the SSR until a reset event happens
counter_state_in<= SRES;
count_wr_in<=SRES;
signal_ok_in<="0";

when others => -- avoiding unexpected behaviour due to bad driving of the inner state
   unlock<='0';
warning<='1';
signal_star_in<=SBLOCK; --Blocking the SSR until a reset event happens
counter_state_in<= SRES;
count_wr_in<=SRES;
signal_ok_in<="0";

 end case;
end if;
end process;

end SSR_beh;

## Counter
library IEEE;
use IEEE.std_logic_1164.all;

entity counter is
generic (N_BIT : integer );
port(
count_clk	: in	STD_LOGIC;
count_reset	: in	STD_LOGIC;
D_in	: in	STD_LOGIC_VECTOR(N_BIT-1 downto 0);
D_out	: out	STD_LOGIC_VECTOR(N_BIT-1 downto 0)
    );
end counter;

architecture Counter_beh of counter is
signal	s_RPCA :	std_logic_vector(N_BIT-1 downto 0);
signal retro_add :	std_logic_vector(N_BIT-1 downto 0);
signal cout_RPCA	:	std_logic;
component RPCA is
generic(Nbit : integer);
port(
a	: in std_logic_vector(Nbit-1 downto 0);
b	: in std_logic_vector(Nbit-1 downto 0);
cin	: in std_logic;
s	: out std_logic_vector(Nbit-1 downto 0);
cout: out std_logic
);
end component;

component DFF is
generic(N_bit : integer);
port (
clk: in std_logic;
reset: in std_logic;
D: in std_logic_vector(N_bit-1 downto 0);
Q: out std_logic_vector(N_bit-1 downto 0)
);
end component;

begin
rpca1	: RPCA
generic map(Nbit => N_BIT)
port map(D_in,retro_add,'0',s_RPCA,cout_RPCA);

dff1	: DFF
generic map(N_bit => N_BIT)
port map(count_clk,count_reset,s_RPCA,retro_add);
counting_proc: process(retro_add)
begin
D_out<=retro_add;
end process;
end Counter_beh;
# Test_benches
## Correct sequence Testbench
library IEEE;
use IEEE.std_logic_1164.all;

entity SSR_tb is
end SSR_tb;

architecture SSR_tb_beh of SSR_tb is

constant T_CLK : time := 10 ns; -- Clock period
constant T_RESET : time := 21 ns; -- Period before the reset deassertion
constant T_FIRST : time := 13 ns; -- Period before the reset deassertion

signal clk_tb	: std_logic := '0'; -- clock signal, intialized to '0'
signal rst_tb	: std_logic := '0'; -- reset signal
    signal in_tb	: std_logic_vector(7 downto 0) ;
signal f_tb	: std_logic :='0';
signal out_tb	: std_logic;
signal warn_tb	: std_logic;

component SecureSequenceRec is
port (
clock:	in std_logic; --- clock signal
reset:	in std_logic; -- reset signal active low
first:	in std_logic; -- start sampling signal
num_in:	in std_logic_vector(7 downto 0); --input sequence number

unlock:	out std_logic; -- signal of success
warning: out std_logic -- error signal

);
end component;
begin

clk_tb <= not(clk_tb) after T_CLK / 2;
rst_tb <= '1' after T_RESET; -- Deasserting the reset after T_RESET nanosecods.

SSR_test: SecureSequenceRec
port map(clk_tb,rst_tb,f_tb,in_tb,out_tb,warn_tb);

r_process:process
begin
wait for T_RESET;
in_tb<="00100100";
wait for T_FIRST;
f_tb<='1';
wait for T_CLK;
f_tb<='0';
in_tb<="00010011"; -- The second is correct
wait for T_CLK;
in_tb<="00111000";
wait for T_CLK;
in_tb<="01100101";
wait for T_CLK;
in_tb<="01001001";

end process;

end SSR_tb_beh;

Picture 3: Simulation of a correct Sequence

## Wrong sequence Testbench
library IEEE;
use IEEE.std_logic_1164.all;

entity SSR_tb is
end SSR_tb;

architecture SSR_tb_beh of SSR_tb is

constant T_CLK : time := 10 ns; -- Clock period
constant T_RESET : time := 21 ns; -- Period before the reset deassertion
constant T_FIRST : time := 13 ns; -- Period before the reset deassertion

signal clk_tb	: std_logic := '0'; -- clock signal, intialized to '0'
signal rst_tb	: std_logic := '0'; -- reset signal
    signal in_tb	: std_logic_vector(7 downto 0) ;
signal f_tb	: std_logic :='0';
signal out_tb	: std_logic;
signal warn_tb	: std_logic;

component SecureSequenceRec is
port (
clock:	in std_logic; --- clock signal
reset:	in std_logic; -- reset signal active low
first:	in std_logic; -- start sampling signal
num_in:	in std_logic_vector(7 downto 0); --input sequence number

unlock:	out std_logic; -- signal of success
warning: out std_logic -- error signal

);
end component;
begin

clk_tb <= not(clk_tb) after T_CLK / 2;
rst_tb <= '1' after T_RESET; -- Deasserting the reset after T_RESET nanosecods.

SSR_test: SecureSequenceRec
port map(clk_tb,rst_tb,f_tb,in_tb,out_tb,warn_tb);

r_process:process
begin
wait for T_RESET;
in_tb<="00100100";
wait for T_FIRST;
f_tb<='1';
wait for T_CLK;
f_tb<='0';
in_tb<="00010011";
wait for T_CLK;
in_tb<="00111000";
wait for T_CLK;
in_tb<="01100101";
wait for T_CLK;
in_tb<="01001001";

end process;

end SSR_tb_beh;

Picture 4: Simulation of a wrong Sequence

# Synthesis on Vivado

risorse utilizzate (slice, LUT, etc.), massima frequenza di funzionamento, cammino critico, etc.